## Slide 1: Team 10: Mesh Filter Pump for Coronary Artery Disease Patients
Team 10
Cainwyn Leung
Claire HyoJoo Kim
Radhey Patel
Selina Qin

## Slide 2: Background
Coronary Artery Disease
  The narrowing or blockage of the coronary arteries—blood vessels that transport oxygenated blood to the heart muscle
  Caused by the buildup of cholesterol and fatty deposits, called atherosclerotic plaques, inside the arteries
  This causes chest pain (angina) or a heart attack

## Slide 3: Background
Issues in Current Coronary Stent Technique
  In-stent Restenosis
    Formation of (neointimal) tissue inside the stent, triggered by vessel injury and the inflammatory response
    May result in re-narrowing of the coronary arteries
  Question in its long-term safety
    Possibility for the late occurrence of thrombosis, blood clot forming in a blood vessel
Affected Population
  Patients who have undergone angioplasty/stent insertions

## Slide 4: Existing Solutions
Sternotomy:
  Used a lot for heart procedures
  Leaves a large scar
  Highly invasive
  Risks include infections, hemorrhage, dysrhythmia
  Long recovery time
  This technique is the most one of the oldest techniques to treat CAD, and it is considered a big surgery in treating blood clotting
Bare-metal Stent (BMS) & Drug eluting stent/ biodegradable stent(DES)
  BMS insertion are the most common technology to treat heart clots, though it is far from being perfect
  Have side effects of re-obstruction of more clots at the stent sites after the placement
  Patients also need to take medication for the stent even after replacement to prevent re-clotting, and these medications can sometimes have side effects as well

## Slide 5: Existing Solutions
  Thrombolysis
    A medication that is given 4-6 hours prior to a stroke
    High death rate
    May cause bleeding in the brain and happens one in 25 people 7 days within thrombolysis and is fatal about 1 in 40 cases
  Thrombectomy
    An endovascular procedure where a mesh is inserted by a catheter into the artery of clot and removes the clot altogether (X-ray imaging used continuously during the procedure).
      This needs to be done within 5 hours of the stroke
      Only works for large arteries
      Risks of having respitory compromise and cranial nerve injury
      Doesn't fully cure blood clot problems; re-obstruction occurs

## Slide 6: Stakeholder Analysis

## Slide 7: Needs Statement
A way to prevent re-obstruction in existing stents for patients who have undergone angioplasty in order to reduce the risk of recurrence of strokes.

## Slide 8: Design Solution Ideas
Inducer/Impeller Rotor
Diffuser
Internal Catheter
Filtration Mesh
Motorization Mechanism

## Slide 10: Insertion/Application

## Slide 11: Questions
What kind of materials would be suitable?
How to stabilize pressure differential through the filtration mechanism?
What risks need to be assessed?
How should we manage the mechanical component of the filtration system while it's in the blood vessel?”